Published in: Atmospheric and Oceanic Optics, Vol. 16, No. 3, 2003, pp.256-261

The GEISA Spectroscopic Database System Revisited For IASI Direct Radiative Transfer Modelling

# N. Jacquinet-Husson*, N.A. Scott*, A. Chédin*, and A.A. Chursin**

*Laboratoire de Météorologie Dynamique, Ecole Polytechnique, 91128 Palaiseau, France,

**Institute of Atmospheric Optics, 634021, Tomsk, Russia

#### Introduction

High resolution vertical infrared sounding new instruments, like AIRS (Atmospheric Infrared Sounder: http://www-airs.jpl.nasa.gov/) in the USA, and IASI (Infrared Atmospheric Sounding Interferometer: http://smsc.cnes.fr/IASI/index.htm) in Europe, which have a better vertical resolution and accuracy compared to the presently existing ones, will mainly be devoted to operational meteorology associated with Numerical Weather Prediction, with the purpose of providing an improved knowledge of the vertical atmospheric structure and of surface properties.

The performances of these second generation vertical sounders will be highly dependent on the accuracy to which the spectroscopic parameters of the optically active atmospheric gases are known, since these are essential input in the forward models used to simulate recorded radiance spectra. Consequently, there is a strong requirement for a comprehensive, validated and operational, interactive spectroscopic database. In this context, since 1974 the ARA (Atmospheric Radiation Analysis) group at LMD (Laboratoire de Météorologie Dynamique, France) has developed the GEISA (Gestion et Etude des Informations Spectroscopiques Atmosphériques: Management and Study of Atmospheric Spectroscopic Information) computer accessible database system (Chédin et al.[1]; Husson et al.[2] [3]), to perform reliable radiative transfer calculations, using a « line-by-line and layer-by-layer » approach for fast forward radiative transfer modelling. This effort benefits the communities doing direct and inverse radiative transfer studies. Currently, GEISA is involved in activities related to the assessment of improved atmospheric sounders capabilities, as described in Jacquinet-Husson et al.[4].

##### GEISA Spectroscopic Database Overview

The GEISA database, in its 1997 version (GEISA-97), is extensively described in Jacquinet-Husson et al. [5]. It has been partially updated in 2001 (GEISA-01). The GEISA-01 system comprises three sub-databases, i.e.:

- The GEISA-01 sub-database on line transition parameters:

GEISA-01 line transition parameters sub-database involves 42 molecules (96 isotopic species) and contains 1,361,667 entries (15,401 supplementary entries since GEISA-97), between 0 and 22,656 cm-1.

The included molecules are of interest for the Earth and other Planet atmospheres (such as: C2H4, GeH4, C3H8, C2N2, C4H2, HC3N, H2S, HCOOH and C3H4, for the Giant Planets). Among the spectroscopic parameters archived in GEISA, the most important for atmospheric radiative transfer modelling are: the wavenumber (cm-1) of the line associated with a vibro-rotational transition, the intensity of the line (cm molecule-1 at 296K), the Lorentzian collision halfwidth (cm-1 atm-1 at 296 K), the energy of the lower level of the transition (cm-1), the transition quantum identifications for the lower and upper levels of the transition, the temperature dependence coefficient of the halfwidth, the database management identification codes for isotopes and for molecules. These parameters are stored following the GEISA usual standard as described in [5].

Three molecules have been updated in GEISA-01, i.e.:

H2O: 10,755 transitions by Toth [6] [7] [8] [9] [10] [11], and Toth et al. [12], have replaced the corresponding existing ones, in the spectral range 500 - 2900 cm-1

CO2: 48,000 new transitions by Tashkun et al. [13] [14] [15] and Teffo et al. [16], have replaced the corresponding existing ones, in the spectral range 430 - 2820 cm-1

N2O: a technical update has removed 118 duplicated lines in the spectral interval 564 cm-1 - 629 cm-1.

- The GEISA-01 sub-database on absorption cross-sections:

Besides the line transition parameters data catalog itself, GEISA includes, in the spectral range 556.380-1763.642 cm-1, a second catalog, referred to as GEISA_CROSS, providing, at various temperatures and pressures, the cross-sections of species exhibiting dense spectra , not suitable for a discrete parameterized format. This represents 4,716,743 entries related to 23 molecules, i.e.: CFC11, CFC12, CFC13, CFC14, CFC113, CFC114, CFC115, HCFC22, HCFC123, HCFC124, HFC125, HFC134a, HCFC141b, HCFC142b, HFC152a, HCFC225ca, HCFC225cb, HFC32, HFC143a, HFC134, N2O5, SF6, ClONO2.

The absorption cross-sections are determined through the following expression:

where ( is the wavenumber (cm-1); ((() is the absorption cross-section (cm2 molecule-1); I0(( ) and I(( ) are the intensities, at the frequency (, of the incident and transmitted radiation, respectively; n is the concentration of the molecules (molecule cm-3) and l the optical path length (cm). It is the ((() value, derived from high-resolution experimental data, that is cataloged in the GEISA cross-sections file.

A management program, supplied with GEISA_CROSS, has been designed to use and manage this sub-database.

No update occurred since the GEISA-97 Edition.

- The GEISA-01 sub-database on micro-physical and optical properties of atmospheric aerosols.

This new GEISA-01 edition sub-database on micro-physical and optical properties of atmospheric aerosols is described in the next section  (GEISA/IASI database).

Users friendly management softwares (Chédin et al.[17]; Husson et al.[3]) are associated with each of these three GEISA-01 sub-databases catalog. The current edition of the GEISA system, with associated softwares, are accessible freely via the ARA/LMD group workstations Web site, upon prior request for password at:

nicole.jacquinet@lmd.polytechnique.fr

GEISA/IASI Database Description

- General Context of the geisa/iasi-01 database

The GEISA/IASI database derives from GEISA as described in Jacquinet-Husson et al. [4] [18]. GEISA/IASI is being elaborated with the purpose of assessing the IASI measurements capabilities, within the ISSWG (IASI Sounding Science Working Group), in the frame of CNES (Centre National d'Etudes Spatiales, France)/EUMETSAT (EUropean organization for the exploitation of METeorological SATellites) European Polar System (EPS), by simulating high resolution radiance spectra and/or experimental data. To benefit as soon as possible from improvements in the knowledge of spectroscopic parameters and to ensure the continuous upgrade and maintenance of GEISA/IASI during the fifteen years of life of the IASI instrument, EUMETSAT and CNES have created a GEISA/IASI Database Scientific Committee (GIDSC). EUMETSAT is planning to implement GEISA/IASI into the EPS ground segment.

The GEISA/IASI database, in its 2001 edition (GEISA/IASI-01), is both an extraction within the IASI or AIRS spectral range (600 - 3000 cm-1) and a partial update of GEISA-97 and GEISA-01, with a similar structure, including the three independent sub-databases described above, i.e.:

- GEISA/IASI-01 Sub-database on Line Transition Parameters

GEISA/IASI-01 line transition sub-database contains spectroscopic line parameters stored following the GEISA usual standard with extended line parameter information (including associated error estimations), for 14 molecules (53 isotopic species) representing 650,274 entries. The GIDSC selected molecules are: H2O, CO2, O3, N2O, CO, CH4, O2, NO, SO2, NO2, HNO3, OCS, C2H2, N2.

It has to be noticed that in GEISA/IASI, CH3D is considered as an isotope of CH4. It is considered as an independent molecule in GEISA-97 and in GEISA-01 The GEISA/IASI-01 content is given in Table 2. The items listed for each molecular species, given in column 1, are: the identification code (ID codes defined for the GEISA management software), the number of lines, the intensity average, the mean line halfwidth at half maximum, the identification codes of the actual molecule various isotopes, and for each isotope: the number of lines, the spectral range (in cm-1) covered by the transitions, and the lines intensities minimum and maximum values (in cm molecule-1), in columns 2 to 11, respectively.

Since the GEISA-97 and GEISA-01 issues, updates have been made in GEISA/IASI-2001, for the spectroscopic line parameters of:

H2O: This update is similar with the one made in GEISA-01

CO2: This update issimilar to the one made in GEISA-01

O3:    Wagner et al. [19], De Backer-Billy and Barbe [20]

CH4: Devi et al. [21], Fejard et al. [22], Hilico et al. [23] [24],

Jouvard et al. [25], Nikitin et al. [26], Ouardi et al. [27], Smith et al. [28]

HNO3: Goldman [29].

C2H2: Mandin et al.[30].

All the archived data can be handled through the database associated general GEISA user-friendly management software.

- GEISA/IASI-01 Sub-database on Absorption Cross-Sections

In this file, referred to as GEISA_CROSS/IASI-01, six molecular species, among the 23 present in GEISA-97 and in GEISA-01, have been selected. These are : CFC-11, CFC-12 (Li and Varanasi [31]; Varanasi and Nemtchinov [32], CFC-14 (Nemtchinov and Varanasi [33], CCl4 (Nemtchinov and Varanasi [34]), N2O5 (Massie et al. [35]) and HCFC-22 (Varanasi et al. [36]; Clerbaux et al. [37]). The content of this sub-database is summarised in Table 2. In the 1st column are listed the molecules included with their name and corresponding chemical formula; columns 2 and 3 provide the cross-section spectral intervals availability and temperature conditions; the related author references are in column 4. The format of the database entries is similar to the GEISA-97 and GEISA-01 ones.

A program, supplied with GEISA_CROSS/IASI, has been designed to use and to manage the data on CFC-11, CFC-12, CFC-14, CCl4 N2O5 and HCFC-22 absorption cross- sections. It is similar to the GEISA-CROSS-97 and GEISA-01 ones.

- GEISA/IASI-01 Sub-database on Micro-physical and Optical Properties of Atmospheric Aerosols

Besides the molecular species which define the gaseous infrared opacity in the Earth’s atmosphere aerosol particles however also contribute to this opacity. Consequently, a common GEISA and GEISA/IASI aerosol sub-database, referred to as GEISA_AEROS, has been recently elaborated. It gathers the micro-physical and optical properties from four published aerosol data catalogs, i.e.: Massie [38], Rublev [39], Hess et al. [40], Köpke et al. [41], the overall content of which deals with the archive of complex refractive indices and possibly computed optical related properties, for selected basic aerosol components. Softwares for data management and user-selected aerosol mixtures elaboration are available from [39] [40] and [41].

The GEISA_AEROS sub-database consists in the following:

- A database on refractive indices of 10 varieties of basic aerosol components

This database, updated by Massie in 2000, since its origin [38] comprises an extensive archive of complex refractive indices, determined both in situ and in the laboratory, from spectral transmission and reflection measurements (over 40 references), of various aerosol components.

- A database microphysical and optical properties of atmospheric aerosols [39]

The first part of the archive consists in complex indices of refraction of seven basic aerosol components, from Zolatarev [42], i.e.: dust-like, water-soluble, soot, and oceanic salt particles, sulfuric acid solution droplets, volcanic ash, and water, which have been used in [39] for the computation of aerosol integrated optical properties, i.e.: extinction coefficient, single scattering albedo, asymmetry factor.

In the second part, the so-called AERCOMP (FORTRAN code) software package, allowing the determination of optical properties for user-defined aerosol mixtures, has been archived with its associated basic aerosol constituent optical properties (including scattering phase functions, as well) files.

- The database and associated software package OPAC (Optical Properties of Aerosols and Clouds) [40].

The first part of this archive is a data set of microphysical properties and the resulting optical properties of:

- Ten basic aerosol components: insoluble, soot, water soluble, two sea salt modes - various kinds of salt contained in seawater-, three mineral modes - mixture of quartz and clay minerals-, mineral transported, sulfate droplets.

- Six water clouds: stratus (continental and maritime), cumulus (continental -clean and polluted- and maritime), fog, and three kinds of cirrus ice clouds, both in the solar and terrestrial spectral range.

The second part is a FORTRAN program making it possible to extract data from the above archive and allowing calculation of any user-defined mixtures of these components. A set of computed typical mixtures is archived, as well.

- The Global Aerosol Data Set GADS [41].

Using the OPAC aerosol archive, GADS provides the related global aerosol distribution as climatologically averaged values both for the winter (December through February) and summer (June through August) seasons on a global grid with a resolution of 5° by 5° longitude and latitude, independently for the components selected in OPAC. A GADS database associated FORTRAN program has been designed to manage the archived data and to make it possible to calculate the global distributions of user- selected aerosol optical or microphysical properties.

The GEISA/IASI spectroscopic database system described above, including data files and management softwares, is available at:

ftp://ara01.lmd.polytechnique.fr/pub/geisa/iasi2001

Table1: Detailed content of GEISA/IASI-01 Line Transition Parameters Sub-database

| Mol. | MolID | #Lines | Intensity Average (cm mol-1) | Alpha average (cm-1) | Iso. ID | #Lines | Fmin (cm-1) | Fmax (cm-1) | Int. min (cm mol-1) | Int. max (cm mol-1) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| H2O | 1 | 13279 | 8.112E-22 | 0.0655 | 161 162 171 181 182 172 | 5218 4584 1203 1661 438 175 | 600.104 604.366 599.702 604.933 1173.772 1234.235 | 2999.854 2999.340 2999.532 3001.175 1684.226 1598.766 | 9.010E-28 1.000E-27 1.490E-27 2.025E-27 2.033E-27 2.033E-27 | 2.989E-19 2.505E-23 1.210E-22 6.051E-22 5.083E-26 9.319E-27 |
| CO2 | 2 | 50375 | 2.185E-21 | 0.0711 | 626 636 628 627 638 637 828 728 838 | 18614 7517 11912 7575 1833 1346 994 288 296 | 599.222 599.026 599.007 599.183 599.165 599.008 615.974 626.438 2115.685 | 2488.222 2395.279 2826.650 2806.198 2605.481 2314.307 2350.898 2358.226 2276.481 | 3.440E-39 1.820E-39 1.390E-36 1.000E-27 3.704E-27 3.708E-27 1.760E-40 3.866E-27 4.870E-42 | 3.530E-18 3.750E-20 6.850E-21 1.250E-21 7.227E-23 1.361E-23 1.309E-23 2.495E-24 1.760E-25 |
| O3 | 3 | 151775 | 1.141E-22 | 0.0701 | 666 668 686 667 676 | 124863 13728 4858 5515 2811 | 600.179 640.037 640.141 599.123 599.382 | 3000.984 1177.493 1145.690 820.380 822.795 | 1.010E-26 9.680E-26 9.620E-26 3.561E-27 3.527E-27 | 4.090E-20 7.760E-23 7.560E-23 5.570E-25 6.057E-25 |
| N2O | 4 | 18938 | 3.634E-21 | 0.0744 | 446 447 448 456 546 | 13273 791 1596 1623 1655 | 599.027 599.420 599.321 599.826 599.129 | 2836.125 2560.588 2543.215 2595.681 2585.207 | 8.260E-27 6.180E-26 1.226E-25 1.218E-25 1.214E-25 | 1.003E-18 4.154E-22 2.045E-21 3.666E-21 3.601E-21 |
| CO | 5 | 3674 | 2.749E-21 | 0.0467 | 26 27 28 36 38 37 | 1499 229 240 1263 226 217 | 1523.979 1831.283 1797.966 1544.497 1779.750 1807.871 | 2316.048 2278.721 2254.309 2259.947 2196.287 2221.114 | 6.840E-70 1.248E-36 1.253E-36 1.880E-65 1.503E-36 1.030E-36 | 4.461E-19 1.602E-22 8.317E-22 4.685E-21 8.698E-24 1.679E-24 |
| CH4 | 6 | 121282 | 6.890E-23 | 0.0498 | 211 311 212 | 68777 22688 29817 | 922.651 998.884 855.753 | 3000.999 3000.999 3000.997 | 1.000E-27 9.488E-28 6.158E-29 | 1.202E-19 1.344E-21 3.658E-23 |
| O2 | 7 | 435 | 2.191E-29 | 0.0466 | 66 | 435 | 1366.105 | 1717.235 | 1.100E-35 | 1.490E-28 |
| NO | 8 | 26083 | 1.767E-22 | 0.0528 | 46 48 56 | 24705 679 699 | 599.089 1601.909 1609.585 | 3000.718 2038.846 2060.462 | 1.401E-85 4.190E-28 4.430E-28 | 6.211E-20 1.390E-22 2.550E-22 |
| SO2 | 9 | 22301 | 1.566E-21 | 0.1132 | 626 646 | 22014 287 | 599.173 2463.470 | 2787.861 2496.088 | 5.000E-26 9.736E-24 | 6.094E-20 3.428E-23 |
| NO2 | 10 | 68252 | 9.087E-22 | 0.0666 | 646 | 68252 | 599.083 | 2938.381 | 9.470E-26 | 1.302E-19 |
| HNO3 | 13 | 152586 | 6.928E-22 | 0.1101 | 146 | 152586 | 599.003 | 1769.982 | 1.051E-25 | 3.020E-20 |
| OCS | 20 | 19768 | 5.288E-21 | 0.0898 | 822 623 634 822 623 634 | 11005 3810 2048 955 1593 357 | 814.581 813.860 825.716 818.098 825.659 1972.188 | 2962.986 2926.274 2880.701 2875.829 2930.386 2032.039 | 1.010E-23 1.010E-23 1.008E-23 1.008E-23 1.016E-23 1.010E-23 | 1.077E-18 4.719E-20 1.198E-20 2.089E-21 8.430E-21 5.240E-22 |
| C2H2 | 24 | 1409 | 2.294E-20 | 0.0609 | 221 231 | 1307 150 | 604.774 613.536 | 1469.865 843.872 | 1.371E-27 3.820E-26 | 1.187E-18 1.577E-20 |
| N2 | 33 | 117 | 5.729E-29 | 0.0469 | 44 | 117 | 2001.711 | 2619.230 | 2.330E-34 | 3.410E-28 |
| TOTAL NUMBER OF LINES IN GEISA/IASI-2001: 650,274 |

Table 2: Content of GEISA_CROSS /IASI-01 Sub-database.

| Molecule id. Formula | Spectral interval (cm-1) | Temperatures (K) | References |
| --- | --- | --- | --- |
| CFC11 CCl3F | 810 - 880 cm-1 1050 - 1120 cm-1 | 55 temperatures from 190 to 296 K | Li and Varanasi [31] |
| CFC12 CCl2F2 | 800 - 950 cm-1 1050 - 1200 cm-1 | 52 temperatures from 190 to 296 K | Varanasi and Nemtchinov [32] |
| CFC-14 CF4 | 1250 - 1290 cm-1 | 55 temperatures from 180 to 296 K | Nemtchinov and Varanasi [33] |
| CCl4 | 750 - 812 cm-1 | 32 temperatures from 208 to 296 K | Nemtchinov and Varanasi [34] |
| N2O5 | 557 – 1763 cm-1 | 4 temperatures from 233 to 293 K | Massie et al. [35] |
| HCFC-22 | 750 – 870 cm-1 765 – 1380 cm-1 | 8 temperatures from 216 to 294 K | Varanasi et al. [36] Clerbaux et al. [37] |

References

- A.Chédin, N.Husson and N.A.Scott, “Une banque de données pour l’étude des phénomènes de transfert radiatif dans les atmosphères planétaires: la banque GEISA”, Bulletin d’Information du Centre de Données Stellaires (France), No.22, 121-121(1982)

- N.Husson, B.Bonnet, N.A.Scott and A.Chédin, “Management and study of spectroscopic information: the GEISA program”, JQSRT, No.48, 509-518(1992)

- N.Husson, B.Bonnet, A.Chédin, N.A.Scott, A.A.Chursin, V.F.Golovko and Vl.G.Tyuterev, “The GEISA data bank in 1993. A PC/AT compatible computers’ new version”, JQSRT, No.52, 425-438(1994)

- N.Jacquinet-Husson, N.A.Scott, A.Chédin, B.Bonnet, A.Barbe, Vl.G.Tyuterev, J.P.Champion, M.Winnewisser, L.R.Brown, R.Gamache, V.F.Golovko and A.A.Chursin, “The GEISA system in 1996: Toward an operational tool for the second generation vertical sounders radiance simulation”, JQSRT, No.59, 511-527(1998)

- N.Jacquinet-Husson, E.Arié, J.Ballard, A.Barbe, L.R.Brown, B.Bonnet, C.Camy-Peyret, J.P.Champion, A.Chédin, A.A.Chursin, C.Clerbaux, G.Duxbury, J-M.Flaud, N.Fourrié, A.Fayt, G.Graner, R.Gamache, A.Goldman, Vl.Golovko, G.Guelachvilli, J-M.Hartmann, J-C.Hilico, G.Lefèvre, O.V.Naumenko, V.Nemtchinov, D.A.Newham, A.Nikitin, J.Orphal, A.Perrin, D.C.Reuter, L.Rosenmann, L.S.Rothman, N.A.Scott, J.Selby, L.N.Sinitsa, J.M.Sirota, A.M.Smith, K.M., Smith, Vl.G.Tyuterev, R.H.Tipping, S.Urban, P.Varanasi and M.Weber, “The 1997 spectroscopic GEISA databank”, JQSRT,No.62, 205-254(1999)

- R.A.Toth, “Water Vapor Measurements between 590 and 2582 cm-1: line positions and Strengths”, JMS, No.190, 379-396(1998)

- R.A.Toth, “Analysis of line positions and strengths of H2O16 ground and hot bands connecting to interacting upper states: (020), (100), and (001)”, JMS, No.194, 28-42(1999a)

- R.A.Toth, “HDO and D2O low pressure, long path spectra in the 600-3100 cm-1 region, I) HDO Line positions and Strengths”, JMS, No.195, 73-97(1999b)

- R.A.Toth, “HDO and D2O low pressure, long path spectra in the 600-3100 cm-1 region, II) D2O line positions and strengths”, JMS, No.195, 98-122(1999c)

- R.A.Toth, “Air- and N2- Broadening Parameters of HDO and D2O, 709 to 1936 cm-1”, JMS, No.198, 358-370(1999d)

- R.A.Toth, “Air- and N2- Broadening Parameters of water vapor: 604 to 2271 cm-1”, JMS, No.201, 218-243(2000)

- R.A.Toth, L.R.Brown and C.Plymate, “Self-broadened widths and frequency shifts of water vapor lines between 590 and 2400 cm-1”, JQSRT, No.59, 529-562(1998)

- S.A.Tashkun, V.I.Perevalov, J-L.Teffo, L.S.Rothman and Vl.G.Tyuterev, “Global fitting of 12C16O2 vibrational-rotational line positions using the effective Hamiltonian approach”, JQSRT, No.60, 785-801(1998)

- S.A.Tashkun, V.I.Perevalov, J-L.Teffo, Vl.G.Tyuterev, “Global fit of 12C16O2 vibrational-rotational line intensities using the effective operator approach”, JQSRT, No.62, 571-598(1999)

- S.A.Tashkun, V.I.Perevalov, J-L.Teffo, M.Lecoutre, T.R.Huet, A.Campargue, D.Bailly and M.P.Esplin, “13C16O2: Global treatment of vibrational-rotational spectra and first observation of the 2(1+5(3 and (1+2(2+5(3 absorption bands”, JMS, No.200, 162-176(2000)

- J-L.Teffo, C.Claveau, Q.Kou, G.Guelachvilli, A.Ubelman, V.I.Perevalov and S.A.Tashkun, “Line intensities of 12C16O2 in the 1.2-1.4 (m spectral region”, JMS, No.201, 249-255(2000)

- A.Chédin, N.Husson, N.A.Scott, I.Cohen-Hallaleh and Berroir, “The GEISA data bank 1984 version”. Internal Note LMD, n° 127, February 1985, reviewed october 1986

- N.Jacquinet-Husson, N.A.Scott, A.Chédin and A.A.Chursin, “The GEISA-97 spectroscopic database system : its present and future”. In IRS 2000: Current Problems in Atmospheric Radiation, W.L. Smith and Y. Timofeyev Eds. A. Deepak Publ., Hampton, No.147, 663-667(2000)

- G.Wagner, M.Birk, F.Schreier and J-M.Flaud, “Spectroscopic data of the three Ozone fundamentals”, In preparation(2002).

- M.R.De Backer-Billy and A.Barbe, “Absolute intensities of the 10(m bands of 16O3”, JMS, No. 205, 43-53(2001)

- V.M.Devi, D.C.Benner, M.A.H.Smith, “Measurements of air-broadened, N2-broadened, N2-broadened and O2-broadened half-widths and pressure-induced line shifts in the (3 of CH4 –C-134”, Applied Optics, No.30, 287-304(1991)

- L.Fejard, J.P.Champion, J.M.Jouvard, L.R.Brown and A.S.Pine, “The intensities of Methane in the 3-5 (m region revisited”, JMS, No.201, 83-94(2000)

- J.C.Hilico, J-P.Champion, S.Toumi, Vl.G.Tyuterev and S.A. Tashkun, “New analysis of the pentad system of Methane and prediction of the (pentad-pentad) spectrum”, JMS, No.168, 455-476(1994)

- J.C.Hilico, O.Robert, M.Loete, S.Toumi, A.S.Pine and L.R.Brown, JMS (in Press)(2001)

- J.M.Jouvard, B.Lavorel, J-P.Champion and L.R. Brown, “Preliminary analysis of the pentad of 13CH4 from Raman and infrared spectra”, JMS, No.150, 201-217(1991)

- A.Nikitin, J-P.Champion, Vl.G.Tyuterev, L.R.Brown, G.Mellau and M.Lock, “The infrared spectrum of CH3D between 900 and 3200 cm-1; extended assignment and modelling”, J. Mol. Struct., No.517, 1-24(2000)

- O.Ouardi, J.C.Hilico, M.Loete and L.R.Brown, “The hot bands of Methane between 5 and 10 (m”, JMS, No.180, 311-322(1996)

- M.A.H.Smith, C.P.Rinsland, V.M.Devi and D.C.Benner, “Temperature-dependence of broadening and shifts of methane lines in the (4 band”, Spectroch. Acta,No. 48 A, 1257-1272(1992)

- A.Goldman , C.P.Rinsland, A.Perrin and J-M. Flaud, “HNO3 line parameters: 1996 HITRAN update and new results”, JQSRT, No.60, 851-861(1998)

- J-Y.Mandin, V.Dana and C.Claveau, “Line intensities in the (5 band of acethylene 12C2H2”, JQSRT, No.67, 429-446(2000)

- Z.Li and P.Varanasi, “Measurement of the absorption cross-sections of CFC-11 at conditions representing various model atmospheres”, JQSRT, No.52, 137-144(1994)

- P.Varanasi and V.Nemtchinov, “Thermal infrared absorption coefficients of CFC-12 at atmospheric conditions”, JQSRT, No.51, 679-687(1994)

- V. Nemtchinov and P. Varanasi, “Thermal Infrared Absorption Cross-Sections of CF4 for Atmospheric Applications”, JQSRT, in Press(2002)

- V. Nemtchinov and P. Varanasi, “Thermal Infrared Absorption Cross-Sections of CCl4 Needed for Atmospheric Remote-Sensing”, JQSRT, in Press(2002)

- S.T. Massie, A. Goldman, D.G. Murcray, J.C. Gille, “Approximate Absorption Cross-Sections of F12, F11, ClONO2, N2O5, HNO3, CCl4, CF4, F21, F113, F114, and HNO3”, Appl. Opt., No.24, 3426-3427(1985)

- P. Varanasi, Z. Li, V. Nemtchinov, A. Cherukuri, “Spectral Absorption Coefficient Data on HCHC-22 and SF6 for Remote-Sensing Applications”, JQSRT, No.52, 323-332(1994)

- C.Clerbaux, R.Colin, P.C.Simon and C.Granier, “Infrared cross-sections and global warming potentials of 10 alternative hydrohalocarbons”, Journal of Geophysical Research, No.98, D6, 10491-10497(1993)

- S.T.Massie, “Indices of refraction for the HITRAN compilation”, JQSRT, No.52, 501-513(1994)

- A.A.Rublev, “Algorithm and computation of aerosol phase functions”, Internal Note IAE-5715/16 of Russian Research Center Kurchatov Institute, Moscow, Russia(1994)

- M.Hess, P.Köpke and I.Schult, “Optical Properties of aerosols and clouds : the software package OPAC”, BAMS, No.79, 5, 831-844(1998)

- P.Köpke, M.Hess, I.Schult and E.P.Shettle, “Global Aerosol DataSet”. Max-Planck-Institut für Meteorologie. Report No.243, Hamburg, Germany(1997)

- V.M.Zolatarev, V.M.Morozov and E.V. Smirnova, 1984. Optical constants of natural and technology media, 216 pp(in Russian), Leningrad, Russia (1984)